## Slide 1
The 8th east Asian Dam conference
22th Oct. 2014
Welcome to Soyanggang Dam

## Slide 2
Contents
Ⅱ
General Information
I
Climate Change Efforts

## Slide 3
General Information
Ⅰ

## Slide 4
1. General Information
Chuncheon-si, Gangwon province, Korea
1967.04 : Initiated Construction
1973.10 : Completed Construction
1974.08 : Initiated O&M
2 Teams, 50 members
Soyanggang
Dam
Seoul
Busan
Director
Management Team
Construction Team
Daejeon
Location
History
Organization & Personnel
Notes: This is a Korean Peninsula. 소양강댐 is located in the Gang-won province.
The construction was started in 1967. At that time Korea was the period of industrialization.
And it was completed in 1973. it took about 6 years.
Since the completion, K-water has managed this Dam until now.
Our office has 2 teams and 50 members are working here.

## Slide 5
1. General Information
Diagram of Dams in the Han-river

## Slide 6
Flood control, water supply and electric generation
Management of Dam facilities
Water quality management
Social contribution activities
Basin Area : 2,703㎢
Reservoir Area : 70 ㎢
Length of reservoir : 66 ㎞
Adjacent city(1) & counties(4)
(ChunCheon) & (InJe, HongCheon,
YangGu, GoSeong)
1. General Information
Roles
Catchment
Soyanggang
Dam
Notes: Our main roles are / flood control, water supply and electric generation by using dam.
In addition, we manage dam and subsidiary facilities as well as water quality.
And we also do various social contribution activities.
Next, let’s look at this map
The blue line means the boundary of the basin.
The area is 2,703 square kilo meters.
When the water level comes to flood water level, the reservoir area is 70 square kilo meters

## Slide 7
1. General Information
Rock
Sand
&
Gravel
540m
Crest EL.203m
Flood water Lev 198.0m (2.9bil㎥)
Restricted Lev during flood 190.3m
EL.80m
Flood Control Capacity
Normal high Lev 193.5m
Dead water Lev 130.0m
Low water Lev 150.0m
Clay
Filter
Dam Type : Earth Core Rockfill Dam
Height / Length : 123m / 530m
Gates : B13m * H13m * 5EA
B14.7m * H14m * 4EA
Generator : 100,000kW * 2EA
Structure
Notes: This picture is the cross section of 소양강댐.
The type of dam is earth core rock-fill dam.
As you see from the center, It is made of clay, filter, sand & gravel and rock.
The Dam’s height is 123m and length is 530m
And the spillway is located in left side of the dam. It has 5 gates. The width is 13m and the height is 13m.
Okay, Next, I’ll explain the water level of 소양강댐
The flood water level is this red line. The designed flood frequency is 200-year.
In this case, we can store 2.9bil ㎥ of water.
And normal high water level is 193.5m, restricted water level during flood is 190.3m

## Slide 8
Flood reduction (12,620 → 5,500 ㎥/sec)
Preventing cities in downstream from flooding (i.e. : Seoul)
Supplying water to downstream areas (i.e. : Seoul & Incheon, etc.)
Preventing droughts in downstream areas
Can be used by 100,000 families / yr
Is equivalent to 160,000-barrel of oil consumption
Flood Control : 500 mil. tons
Water Supply : 1,213 mil. tons/yr
Generation : 353 GWh/yr
1. General Information
Benefits
Notes: The benefit of 소양강댐 is like this.
First, we can control downstream flood.
So the downstream areas such as Seoul, 춘천 are protected safely from the flood.
Second, we can supply sufficient water to downstream
The amount is 1,213mil tons per annum
Third, we can produce clean energy without any pollution.
The amount is 353GWh/annum
It is equal to save 160,000 barrel of oil

## Slide 9
2. Providing Support to the adjacent areas
Supporting Farming machines
Promoting welfare
English village
K-water supports areas around Dams through various works.
(Amount : approximately 7mil. $)
Hosting Mini Concerts at the Dam’s Square
Overview

## Slide 10
3. Plans to make the Dam more attractive
Facilities Improvement
Remodeling of exhibition hall
Opening of Dam crest road to tourists
Scenic lighting

## Slide 11
Climate change Efforts
Ⅱ

## Slide 12
1. The Enhancement of the Flood Control Capacity
Installation of an auxiliary spillway for hydrological stability
Climate changes (’84, ’90 Flood, Typhoon ‘Lusa’ etc)
Reinforcement of dam design standard (Freq. 1,000yr → PMF)
Hydrological instability (’99 Precise diagnosis of safety)
Before
As Is
810
632
Rainfall (mm/2days)
20,700
12,400
Max inflow (CMS)
14,200
7,500
Max discharging (CMS)
Before
As Is
Before
As Is
Hydrological Factor Comparison
Background
Notes: First issue is “the Enhancement of the Flood Control Capacity”.
As you know, because of climate change, strong floods and rainfalls occurred more often than before.
So the design factors of dam had to be changed.
For example, PMP, PMF
So we couldn’t assure the dam’s safety.
Finally we decided to make another spillway for hydrological stability of dam.

## Slide 13
Parking Lot
Exhibition hall
Square park
observatory
Inlet
Outlet
Ecological Park
Dam
Plant
Spillway
Access Road
 Structure : low-slope tunnel type spillway
 Tunnel size : D14m x 2ea(L1=1,276m, L2=1,206m)
 Max outflow : 6,700㎥/s (Spillway 7,500㎥/s)
 Construction period : 2004 ~ 2010
 Construction cost : 174.3 bil. Won ($154 mil.)
Aerial view
Notes: This is an aerial view of 소양강댐.
this is the auxiliary spillway which is low-slope tunnel type.
It consists of 2 Tunnels, and diameter is 14m. The length is about 1,200m
Max outflow of these tunnel is 6,700 tons
The construction period is from 2004 to 2010.
The cost is 154 mil. US dollars.

## Slide 14
DAM
3km
8km
12km
18km
23km
33km
43km
’07. 8. 13
Turbid water Inflow
Highly turbid water inflow after heavy rainfalls in ’06 ~ ’07
- Max turbidity : 328 NTU
- Discharging duration : 226 days(<10NTU)
Soil loss from landslide, roads and river bank loss by heavy rain
Sand and clay loss from alpine region farm
2. The facility of a Selective Intake
Status
Causes
Notes: And the second issue is the facility of a selective intake which is under construction, now.
In 2006 Summer, Highly turbid water inflowed into Soyanggang Dam after strong heavy rain.
It took about 226 days to make water quality below 10NTU.

## Slide 15
Exhibition hall
Square park
Parking lot
Existing intake tower
New intake tower
 Tunnel type : circle(D=7.3m, L=62.0m)
 Building size : W16m × L22.2m × H89.2m
 Gate type : W10m × H14m × 3 ea
 Construction period : 2009.12. ~ 2015. 12.
 Construction cost : 47.2 bil. won ($ 44 mil.)
2. The facility of a Selective Intake
Bird’s eye view
Notes: This is an bird’s eye view.
Tunnel type is circular. The diameter is 7.3m and the length is 62.0m.

## Slide 16
Thank You
K-water is creating a happier world with water